## Slide 1: Overview
Gate Circuits and Boolean Equations
  - Binary Logic and Gates
  - Boolean Algebra
  - Standard Forms
Additional Gates and Circuits
  - Other Gate Types
  - Exclusive-OR Operator and Gates
  - High-Impedance Outputs

## Slide 2: Binary Logic and Gates
Digital circuits are hardware components (based on transistors) that manipulate binary information
We model the transistor-based electronic circuits as logic gates.

## Slide 3: Binary Logic
Binary variables take on one of two values.
Logical operators operate on binary values and binary variables.
Basic logical operators are the logic functions AND, OR and NOT.
Logic gates implement logic functions.
Boolean Algebra: a useful mathematical system for specifying and transforming logic functions.

## Slide 4: Binary Variables
Recall that the two binary values have different names:
  True/False
  On/Off
  Yes/No
  1/0
We use 1 and 0 to denote the two values.

## Slide 5: Conclusion
Computers are implementations of Boolean logic.
Boolean functions are completely described by truth tables.
Logic gates are small circuits that implement Boolean operators.
The basic gates are AND, OR, and NOT.
  The XOR gate is very useful in parity checkers and adders.
The “universal gates” are NOR, and NAND.

## Slide 6: Logical Operations
The three basic logical operations are:
  AND
  OR
  NOT
AND is denoted by a dot (·).
OR is denoted by a plus (+).
NOT is denoted by an overbar ( ¯ ), a single quote mark (') after, or (~) before the variable.

## Slide 7: Notation Examples
Examples:
  is read “Y is equal to A AND B.”
  is read “z is equal to x OR y.”
  is read “X is equal to NOT A.”
Note: The statement:
  1 + 1 = 2 (read “one plus one equals two”)
is not the same as
  1 + 1 = 1 (read “1 or 1 equals 1”).
=
B
A
Y
×
y
x
z
+
=
A
X
=

## Slide 8: Operator Definitions
Operations are defined on the values "0" and "1" for each operator:
AND
0 · 0 = 0
0 · 1 = 0
1 · 0 = 0
1 · 1 = 1
OR
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 1
NOT
1
0
=
0
1
=

## Slide 9: Truth Tables
0
1
1
0
X
NOT
X
Z
=
Truth table - a tabular listing of the values of a function for all possible combinations of values on its arguments
Example: Truth tables for the basic logic operations:
1
1
1
0
0
1
0
1
0
0
0
0
Z = X·Y
Y
X
AND
OR |  | 
X | Y | Z = X+Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 10: Basic Theorems

## Slide 11: Logic Function Implementation
Using Switches
  For inputs:
    logic 1 is switch closed
    logic 0 is switch open
  For outputs:
    logic 1 is light on
    logic 0 is light off.
  NOT uses a switch such
  that:
    logic 1 is switch open
    logic 0 is switch closed
Switches in series => AND
Switches in parallel => OR
C
Normally-closed switch => NOT

## Slide 12: Review of Boolean algebra
Not is a horizontal bar above the number
  0 = 1
  1 = 0
Or is a plus
  0+0 = 0
  0+1 = 1
  1+0 = 1
  1+1 = 1
And is multiplication
  0*0 = 0
  0*1 = 0
  1*0 = 0
  1*1 = 1
_
_

## Slide 13: Logic Gate

## Slide 14: Logic Gate
A gate is an digital circuit which operates on one or more signals and produce single output.
Gates are digital circuits because the input and output signals are denoted by either 1(high voltage) or 0(low voltage).
There are three basic gates and are:
1. AND gate
2. OR gate
3. NOT gate

## Slide 15: AND gate
The AND gate is an electronic circuit that gives a high output (1) only if all its inputs are high.
AND gate takes two or more input signals and produce only one output signal.
Input A | Input B | Output AB
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 16: OR gate
The OR gate is an electronic circuit that gives a high output (1) if one or more of its inputs are high.
OR gate also takes two or more input signals and produce only one output signal.
Input A | Input B | Output A+B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 17: NOT gate
The NOT gate is an electronic circuit that gives a high output (1) if its input is low .
NOT gate takes only one input signal and produce only one output signal.
The output of NOT gate is complement of its input.
It is also called inverter.
Input A | Output A
0 | 1
1 | 0

## Slide 18: DeMorgan’s Theorem
(x + y)’ = x’y’ ,(xy)’ = x’ + y’
By means of truth table
x | y | x’ | y’ | x+y | (x+y)’ | x’y’ | xy | x’+y' | (xy)’
0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1
1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0

## Slide 19
NAND Gate
Known as a “universal” gate because ANY digital circuit can be implemented with NAND gates alone.

## Slide 20
NAND Gate
NAND
X
Y
Z
X Y Z
0 0 1
0 1 1
1 0 1
1 1 0
Z = ~(X & Y)
Nand(Z,X,Y)

## Slide 21
NAND Gate
X
X
F = (X•X)’
= X’+X’
= X’
X
Y
Y
F = ((X•Y)’)’
= (X’+Y’)’
= X’’•Y’’
= X•Y
F = (X’•Y’)’
= X’’+Y’’
= X+Y
X
X
F = X’
X
Y
Y
F X•Y
F = X+Y

## Slide 22
NOR Gate
NOR
X
Y
Z
X Y Z
0 0 1
0 1 0
1 0 0
1 1 0
Z = ~(X | Y)
nor(Z,X,Y)

## Slide 23
Exclusive-OR Gate
X Y Z
XOR
X
Y
Z
0 0 0
0 1 1
1 0 1
1 1 0
Z = X ^ Y
xor(Z,X,Y)

## Slide 24
Exclusive-NOR Gate
X Y Z
XNOR
X
Y
Z
0 0 1
0 1 0
1 0 0
1 1 1
Z = ~ (X ^ Y)
Z = X ~ ^ Y
Xnor (Z,X,Y)

## Slide 25: Logic Gate Symbols and Behavior
Logic gates have special symbols:

## Slide 26: AND and OR gates with more than two inputs

## Slide 27: Boolean Algebra
Boolean expression: a expression formed by binary variables, for example,
Boolean function: a binary variable identifying the function followed by an equal sign and a Boolean expression for example

## Slide 28: Truth table and Logic circuit
For the Boolean function
Logic Circuit Diagram

## Slide 29: Basic identities of Boolean Algebra
1.
3.
5.
7.
9.
11.
13.
15.
17.
Commutative
Associative
Distributive
DeMorgan
’
s
2.
4.
6.
8.
X
. 1
X
=
X
. 0
0
=
X . X
X
=
0
=
X . X
An algebraic structure defined on a set of at least two elements together with three binary operators (denoted +, · and - ) that satisfies the following basic identities:
10.
12.
14.
16.
X + Y
Y + X
=
(X + Y)
Z
+
X + (Y
Z)
+
=
X(Y +
Z)
XY
XZ
+
=
X + Y
X . Y
=
XY
YX
=
(XY)
Z
X(Y
Z)
=
X
+ YZ
(X + Y)
(X + Z)
=
X . Y
X + Y
=
X
+ 0
X
=
+
X
1
1
=
X + X
X
=
1
=
X + X
X = X

## Slide 30: Truth Table to Verify DeMorgan’s Theorem
Extension of DeMorgan’s Theorem:

## Slide 31: Boolean Operator Precedence
The order of evaluation in a Boolean expression is:
1.
Parentheses
2.
NOT
3.
AND
4.
OR
Example: F = A (B + C) (C + D)

## Slide 32: Boolean Algebraic Manipulation

## Slide 33: Boolean Algebraic Manipulation
AB + AC + BC = AB + AC (Consensus Theorem)
Proof Steps Justification (identity or theorem)
AB + AC + BC
= AB + AC + 1 · BC
= AB +AC + (A + A) · BC
=
Notes: Justification 1: 1 . X = X
Justification 2: X + X’ = 1
= AB + A’C + ABC + A’BC X(Y + Z) = XY + XZ (Distributive Law)
= AB + ABC + A’C + A’BC X + Y = Y + X (Commutative Law)
= AB . 1 + ABC + A’C . 1 + A’C . B X . 1 = X, X . Y = Y . X (Commutative Law)
= AB (1 + C) + A’C (1 + B) X(Y + Z) = XY +XZ (Distributive Law)
= AB . 1 + A’C . 1 = AB + A’C X . 1 = X

## Slide 34: Example: Complementing Function
By DeMorgan’s Theorem (Example 2-2)
By duality (Example 2-3)
Notes: = X’ Y’ Z + X Y’ (A + B)’ = A’ . B’ (DeMorgan’s Law)
= Y’ X’ Z + Y’ X A . B = B . A (Commutative Law)
= Y’ (X’ Z + X) A(B + C) = AB + AC (Distributive Law)
= Y’ (X’ + X)(Z + X) A + BC = (A + B)(A + C) (Distributive Law)
= Y’ . 1 . (Z + X) A + A’ = 1
= Y’ (X + Z) 1 . A = A, A + B = B + A (Commutative Law)

## Slide 35: Canonical Forms
It is useful to specify Boolean functions in a form that:
  Allows comparison for equality.
  Has a correspondence to the truth tables
Canonical Forms in common usage:
  Sum of Minterms (SOM)
  Product of Maxterms (POM)

## Slide 36: Maxterms and Minterms
Examples: Two variable minterms and maxterms.
The index above is important for describing which variables in the terms are true and which are complemented.
Index | Minterm | Maxterm
0 | x y | x + y
1 | x y | x + y
2 | x y | x + y
3 | x y | x + y

## Slide 37: Minterms
Minterms are AND terms with every variable present in either true or complemented form.
Given that each binary variable may appear normal (e.g., x) or complemented (e.g., ), there are 2n minterms for n variables.
Example: Two variables (X and Y)produce 2 x 2 = 4 combinations:
x

## Slide 38
  (both normal)
  (X normal, Y complemented)
  (X complemented, Y normal)
  X (both complemented)
Thus there are four minterms of two variables.
Y
X
XY
Y
X
Y

## Slide 39: Maxterms
Maxterms are OR terms with every variable in true or complemented form.
Given that each binary variable may appear normal (e.g., x) or complemented (e.g., x), there are 2n maxterms for n variables.
Example: Two variables (X and Y) produce 2 x 2 = 4 combinations:
  (both normal)
  (x normal, y complemented)
  (x complemented, y normal)
  (both complemented)
Y
X
+
Y
X
+
Y
X
+
Y
X
+

## Slide 40: Minterms for three variables

## Slide 41: Maxterms for three variables

## Slide 42: Minterm and Maxterm Relationship
Review: DeMorgan's Theorem
and
Two-variable example:
and
Thus M2 is the complement of m2 and vice-versa.
Since DeMorgan's Theorem holds for n variables, the above holds for terms of n variables
giving:
and
Thus Mi is the complement of mi.
y
x
y
·
x
+
=
y
x
y
x
×
=
+
y
x
M
2
+
=
y
x·
m
2
=
i
m
M
=
i
i
i
M
m
=

## Slide 43: Function Tables for Both
Minterms of 2 variables Maxterms of 2 variables
Each column in the maxterm function table is the complement of the column in the minterm function table since Mi is the complement of mi.
x y
m
0
m
1
m
2
m
3
0 0
1
0
0
0
0 1
0
1
0
0
1 0
0
0
1
0
1 1
0
0
0
1
x y
M
0
M
1
M
2
M
3
0 0
0
1
1
1
0 1
1
0
1
1
1 0
1
1
0
1
1 1
1
1
1
0

## Slide 44: Observations
In the function tables:
  Each minterm has one and only one 1 present in the 2n terms (a minimum of 1s). All other entries are 0.
  Each maxterm has one and only one 0 present in the 2n terms All other entries are 1 (a maximum of 1s).
We can implement any function by "ORing" the minterms corresponding to "1" entries in the function table. These are called the minterms of the function.

## Slide 45
We can implement any function by "ANDing" the maxterms corresponding to "0" entries in the function table. These are called the maxterms of the function.
This gives us two canonical forms:
  Sum of Minterms (SOM)
  Product of Maxterms (POM)
for stating any Boolean function.

## Slide 46: Conversion of Minterm and Maxterm

## Slide 47: Conversion of Minterm and Maxterm

## Slide 48: Canonical Sum of Minterms
Any Boolean function can be expressed as a Sum of Minterms.
  For the function table, the minterms used are the terms corresponding to the 1's
  For expressions, expand all terms first to explicitly list all minterms. Do this by “ANDing” any term missing a variable v with a term ( ).
Example: Implement as a sum of minterms.
  First expand terms:
  Then distribute terms:
  Express as sum of minterms: f = m3 + m2 + m0
y
x
x
f
+
=
y
x
)
y
y
(
x
f
+
+
=
y
x
y
x
xy
f
+
+
=
v
v
+

## Slide 49: Another SOM Example
Expand by using truth table
According to truth table Table 2-8,
Notes: F = A(B + B’)(C + C’) + (A + A’) B’ C
= ABC + ABC’ + AB’C + AB’C’ + AB’C + A’B’C
= ABC + ABC’ + AB’C + AB’C’ + A’B’C
= m7 + m6 + m5 + m4 + m1 = m1 + m4 + m5 + m6 + m7

## Slide 50: Standard Sum-of-Products (SOP)
A sum of minterms form for n variables can be written down directly from a truth table.
  Implementation of this form is a two-level network of gates such that:
  The first level consists of n-input AND gates, and
  The second level is a single OR gate (with fewer than 2n inputs).
This form often can be simplified so that the corresponding circuit is simpler.

## Slide 51: Standard Sum-of-Products (SOP)
Example:
Fig. 2-5
a two-level implementation/two-level circuit
Product-of-Sums (POS):
What’s the implementation?
Notes: F = A’ B’ C + A (B’ C’ + B C’ + B’ C + B C)
= A’ B’ C + A (B’ + B) (C’ + C)
= A’ B’ C + A.1.1
= A’ B’ C + A
= B’C + A

## Slide 52: Convert non-SOP expression to SOP expression
The decision whether to use a two-level or multiple-level implementation is complex.
  no. of gates
  No. of gate inputs
  amount of time delay

## Slide 53: Simplification of two-level implementation of SOP expression
The two implementations for F are shown below – it is quite apparent which is simpler!

## Slide 54: SOP and POS Observations
The previous examples show that:
  Canonical Forms (Sum-of-minterms, Product-of-Maxterms), or other standard forms (SOP, POS) differ in complexity
  Boolean algebra can be used to manipulate equations into simpler forms.
  Simpler equations lead to simpler two-level implementations
Questions:
  How can we attain a “simplest” expression?
  Is there only one minimum cost circuit?
  The next part will deal with these issues.

## Slide 55
POWER CONSUMPTION OF SYSTEM

## Slide 56: Basic Theorem of Boolean Algebra
T1 : Properties of 0
  (a) 0 + A = A (b) 0 A = 0
T2 : Properties of 1
  (a) 1 + A = 1 (b) 1 A = A

## Slide 57: Basic Theorem of Boolean Algebra
T3 : Commutative Law
  (a) A + B = B + A (b) A B = B A
T4 : Associate Law
  (a) (A + B) + C = A + (B + C) (b) (A B) C = A (B C)
T5 : Distributive Law
  (a) A (B + C) = A B + A C (b) A + (B C) = (A + B) (A + C)
  (c) A+A’B = A+B

## Slide 58: Basic Theorem of Boolean Algebra
T6 : Indempotence (Identity ) Law
  (a) A + A = A (b) A A = A
T7 : Absorption (Redundance) Law
  (a) A + A B = A (b) A (A + B) = A

## Slide 59: Basic Theorem of Boolean Algebra
T8 : Complementary Law
  (a) X+X’=1
  (b) X.X’=0
T9 : Involution
  (a) x’’ = x
T10 : De Morgan's Theorem
  (a) (X+Y)’=X’.Y’
  (b) (X.Y)’=X’+Y’

## Slide 60: De Morgan's Theorem 1
Theorem 1 A . B = A + B

## Slide 61: De Morgan's Theorem 1
Theorem 1 A . B = A + B

## Slide 62: De Morgan's Theorem 1
Theorem 1 A . B = A + B

## Slide 63: De Morgan's Theorem 2
Theorem 1 A + B = A . B

## Slide 64: De Morgan's Theorem 2
Theorem 2 A + B = A . B

## Slide 65: De Morgan's Theorem 2
Theorem 2 A + B = A . B

## Slide 66: De Morgan's Theorem 2
Theorem 2 A + B = A . B